## Slide 2: What Is Hyperdimensional Computing?
A Type of Computation Using Operations on Very Large Vectors
  1k to 10k+ elements
Notes: Also known as Vector Symbolic Architecture
1k to 10k+ elements

## Slide 3: What Is Hyperdimensional Computing?
A Type of Computation Using Operations on Very Large Vectors
  1k to 10k+ elements
Has Many Real-World Applications
  Medical Diagnosis
https://www.frontiersin.org/articles/10.3389/fneur.2022.816294/full

## Slide 4: What Is Hyperdimensional Computing?
A Type of Computation Using Operations on Very Large Vectors
  1k to 10k+ elements
Has Many Real-World Applications
  Medical Diagnosis
  Robot Localization
https://www.tu-chemnitz.de/etit/proaut/en/research/vsa.html

## Slide 5: What Is Hyperdimensional Computing?
A Type of Computation Using Operations on Very Large Vectors
  1k to 10k+ elements
Has Many Real-World Applications
  Medical Diagnosis
  Robot Localization
  Text Classification
  Etc.
https://www.researchgate.net/figure/Visualization-of-how-the-Hyperdimensional-Inference-Layer-HIL-2-3-learns-to_fig1_360994078

## Slide 6: Why Use HCD?
Suppose we have some number represented in binary
  What happens if there is a single bit error?

## Slide 7: Why Use HCD?
Suppose we have some number represented in binary
  What happens if there is a single bit error?
Notes: If its in the LSB’s then there is not much of an issue

## Slide 8: Why Use HCD?
Suppose we have some number represented in binary
  What happens if there is a single bit error?
Notes: If it in the MSB’s the entire result can be incorrect
This is because each bit in the number has a specific meaning

## Slide 9: Why Use HDC?
HDC Overcomes this with distributed representations
  An Example with the BSC Encoding
True HV
Errored HV
Similarity Metric = 0.889
Notes: HDC overcomes this with distributed representations
Each number has no specific meaning on its own, but combined with the full vector the meaning can be decerned

## Slide 10: Why Use HDC?
HDC Overcomes this with distributed representations
  An Example with the BSC Encoding
True HV
Errored HV
Similarity Metric = 0.889
Notes: HDC overcomes this with distributed representations
Each number has no specific meaning on its own, but combined with the full vector the meaning can be decerned

## Slide 11: Why Use HDC?
HDC Overcomes this with distributed representations
  An Example with the BSC Encoding
True HV
Errored HV
Similarity Metric = 0.889
Notes: HDC overcomes this with distributed representations
Each number has no specific meaning on its own, but combined with the full vector the meaning can be decerned

## Slide 12: Why Use HDC?
HDC Overcomes this with distributed representations
  An Example with the BSC Encoding
True HV
Errored HV
Similarity Metric = 0.889
Notes: HDC overcomes this with distributed representations
Each number has no specific meaning on its own, but combined with the full vector the meaning can be decerned

## Slide 13: What Operations Does HDC Require?
There Are 3 Main Operations In HDC
  Similarity
  Bundling
  Binding

## Slide 14: What Operations Does HDC Require?
Similarity
  Takes two vectors and returns a single number (ideally between -1 and 1) to tell you how similar the vectors are

## Slide 15: What Operations Does HDC Require?
Bundling
  Takes 2+ inputs and produces an output vector highly similar to all inputs

## Slide 16: What Operations Does HDC Require?
Binding
  Takes 2 inputs and produces an output vector highly dis-similar to both inputs

## Slide 17: How To Accelerate HDC?
Notes: While kernels for each type of operation have some differences, they are largely the same. We will be focusing on the bundling
Most of these HDC encodings are embarrassingly parallel
This allows us to compute bundling, binding, and similarity result elements independently

## Slide 18: How To Accelerate HDC?
Notes: While kernels for each type of operation have some differences, they are largely the same. We will be focusing on the bundling
Most of these HDC encodings are embarrassingly parallel
This allows us to compute bundling, binding, and similarity result elements independently

## Slide 19: How To Accelerate HDC?
Allocate Ports
Notes: While kernels for each type of operation have some differences, they are largely the same. We will be focusing on the bundling
Most of these HDC encodings are embarrassingly parallel
This allows us to compute bundling, binding, and similarity result elements independently

## Slide 20: How To Accelerate HDC?
Allocate Ports
Notes: While kernels for each type of operation have some differences, they are largely the same. We will be focusing on the bundling
Most of these HDC encodings are embarrassingly parallel
This allows us to compute bundling, binding, and similarity result elements independently

## Slide 21: How To Accelerate HDC?
Allocate Ports
Notes: While kernels for each type of operation have some differences, they are largely the same. We will be focusing on the bundling
Most of these HDC encodings are embarrassingly parallel
This allows us to compute bundling, binding, and similarity result elements independently

## Slide 22: How To Accelerate HDC?
Allocate Ports
Release Ports
Notes: While kernels for each type of operation have some differences, they are largely the same. We will be focusing on the bundling
Most of these HDC encodings are embarrassingly parallel
This allows us to compute bundling, binding, and similarity result elements independently

## Slide 23: How To Accelerate HDC?
Allocate Ports
Release Ports
Notes: While kernels for each type of operation have some differences, they are largely the same. We will be focusing on the bundling
Most of these HDC encodings are embarrassingly parallel
This allows us to compute bundling, binding, and similarity result elements independently

## Slide 24: Bundle Kernel Hierarchy

## Slide 25: Memory Mapper

## Slide 26: Element Kernel

## Slide 27: Our Full Architecture Reviewed
Allocate Ports
Release Ports
Notes: While kernels for each type of operation have some differences, they are largely the same. We will be focusing on the bundling
Most of these HDC encodings are embarrassingly parallel
This allows us to compute bundling, binding, and similarity result elements independently

## Slide 28: Questions?

## Slide 29: Bonus Slides
State-Flow Diagrams
  Bundle Kernel
  Element Kernel
  Memory Mapper
Transaction Waveforms
  Bundle Kernel
  Element Kernel
  Memory Mapper
Estimated Resource Usage

## Slide 30: Bundle Kernels State-Flow

## Slide 31: Element Kernel State-Flow

## Slide 32: Memory Mapper State-Flow

## Slide 33: Bundle Kernel Transaction Waveforms

## Slide 34: Element Kernel Transaction Waveforms

## Slide 35: Memory Mapper Transaction Waveforms

## Slide 36: Estimated Resource Usage
Bundle Kernel Mapper
Bundle Kernel Generator
Bundle Kernel
Bundle Memory Mapper