## Slide 1: An Extensible Hyperdimensional Computing Accelerator for Use in Embedded Systems
By: Graham Power

## Slide 2: What Is Hyperdimensional Computing?

## Slide 3: TODO
What Is HDC?
  Also known as Vector Symbolic Architectures
  A type of computation using operations on very large vectors
  1k to 10k+ elements
  Used in applications like
    Medical diagnosis
    Robot localization
    Text classification
    Image classification
    Inference
  Elements can be from many different spaces
    Real
    Binary
    Imaginary

## Slide 4: TODO
Why use HDC?
  Suppose we have some number represented in binary
  What if there is a single bit error?
  If its in the LSB’s then there is not much of an issue
  If it in the MSB’s the entire result can be incorrect
  This is because each bit in the number has a specific meaning
  HDC overcomes this with distributed representations
  Each number has no specific meaning on its own, but combined with the full vector the meaning can be decerned

## Slide 5: TODO
What operations are involved in HDC?
There are 3 main operations involved in HDC
The core of HDC is the similarity comparison
  Takes two vectors and returns a single number (ideally between -1 and 1) to tell you how similar the vectors are
Next there is Bundling
  Group many vectors together
  Takes 2+ inputs and produces an output vector highly similar to all inputs
Binding
  Isolating vectors
  Takes 2 inputs and produces an output vector highly dis-similar to both inputs

## Slide 6: TODO
How to accelerate HDC?
Most of these HDC encodings are embarrassingly parallel
This allows us to compute bundling, binding, and similarity result elements independently
At a high level the accelerator looks like this
  Show top-level block diagram
  While kernels for each type of operation have some differences, they are largely the same. We will be focusing on the
At the bottom we have the bundle kernel
  Show the bundler

## Slide 7: TODO
Data is passed to the bundle kernel using a memory mapper
  Show the memory mapper
Each bundle kernel and memory mapper are paired and controlled by a kernel mapper
  Kernels mappers will run many kernels in parallel
Port Allocator
  So far we’ve assumed every memory mapper has access to the memory, but theres a limited number of ports
  To handle this we add a Port Allocator in between the kernels and the memory. Each port will be mapped to a kernel and the mapping is stored in a port allocation table.
  When a new operation (bundle, bind, similarity) is requested it will wait until enough ports are available and then the ports are locked by the kernels in the port allocation table

## Slide 8: TODO
Memory Architecture
  Hypervectors are stored contiguously in a virtual memory
  Each block ram in the FPGA will store the same 1-2 elements (depending on desired memory size) from all hypervectors in the memory space
  While hypervectors may vary in size, all hypervectors must start from an address which is a multiple of the max hypervector size

## Slide 9: TODO
The top level accelerator will be implemented as an X(3??) stage pipeline
First hypervector requests made will be added the a pre-flight FIFO queue
A scoreboard will be used to filter out instruction dependencies allowing for multiple instructions to be executed at once
Once passed through the pre-flight queue, instructions will be added the an in-flight FIFO queue where they wait for enough ports to be available to begin executing

## Slide 10: TODO
Allocation of ports will also be done using a scoreboard-like process.
Instructions will “lock” a port in the port-table after which it is guaranteed to have uncontested access to the ports for its full execution time
Once complete, the port allocation table and scoreboard will be cleared
We will also have a result validity table to keep track of which hypervectors are *not* produced by any in-queue instruction, meaning the hypervector result is valid and ready to read

## Slide 11: Questions?

## Slide 12: Bonus Slides